## Slide 1: Energy Supply Systems
MADIEGA Séripoughin Aida Justine

## Slide 2: What does Energy Supply Systems cover?
Done / existing | New (2026)
Solar panel monitoring | Carbon footprint calculator
Energy consumption tracking | Generator backup mgmt
Renewable energy mgmt | 
Cost optimization | 

## Slide 3: 01 02 03 04 Extended Energy Consumption
Misc. loads: 15 kWh/day
Lighting: 2 kWh/day
Storage/Cooling: 8 kWh/day
Pump: 6 kWh/day

## Slide 4: 05 06 07 Extended Energy Consumption
Monitoring/IoT: 0.5 kWh/day
Dryer: variable
Security: 1 kWh/day

## Slide 5: PV & Battery Sizing
Scenario | PV (kWp) | Panels | Battery (kWh)
Base | 6,57 | 17 | 15,05
50 kg/day | 36,87 | 93 | 84,49
200 kg/day | 127,78 | 320 | 292,82
1,000 kg/day | 612,63 | 1 532 | 1 403,94

## Slide 6: Example: Solar PV & Carbon Management
Assumptions :
PSH Burkina Faso: 6,6 h
Diesel Cost (LCOE): 0,40 $/kWh
Grid Emission Factor: 0,5 kg CO₂/kWh

## Slide 7
Benefit type | Amount | Details
Diesel savings avoided (solar) | 24 966 $/an | vs. Equivalent diesel generation
Maintenance cost | − 2 063 $/an | 2% of CAPEX
Generator backup cost | − 576 $/an | 180h/an of estimated backup
NET SAVINGS | 22 327 $/an | 
Estimated payback | ~4,7 ans | Based on avoided diesel costs

## Slide 8: Carbon Footprint Reduction

## Slide 9
Benefit type | Amount | Details
Emissions avoided vs. grid | 33 306 kg CO₂/year | Solar vs. equivalent conventional grid
Residual emissions (PV + generator) | 4 411 kg CO₂/Year | PV lifecycle + diesel backup
NET REDUCTION | 86,80% | Compared to 100% grid/diesel power

## Slide 10: Generator Backup Sizing

## Slide 11
Parameter | Value
Critical Load | 9,5 kWh/day
Generator Size | 8 kW
Diesel Cost | 0,40 $/kWh
Annual Usage Hours | 180 h/year
Annual Energy from Generator | 1 440 kWh/year
Annual Generator Cost | 576 $/year
Generator Emission Factor | 0,75 kg CO₂/kWh
Generator Annual Emissions | 1 080 kg CO₂/year
Generator CAPEX | 4 000 $

## Slide 12: Monitoring App Mockup

## Slide 13
Screen | Content
Dashboard | Daily solar production (kWh), % self-consumption
Consumption | Real-time breakdown by system (pump, miscellaneous, storage, lighting, security, dryer)
Generator | Status, cumulative hours, fuel level, cumulative cost
Carbon | Cumulative CO₂ avoided (from Section 7)
Alerts | Panel failure, low battery, generator activation, grid outage

## Slide 14: Next Steps
Distance betweeConfirm the ROI reference price (avoided diesel vs. grid tariff)
Validate the inverter sizing
Decide between monocrystalline vs. polycrystalline

## Slide 15: Thanks for attention!